MICHELIN OFFERS 10 TIPS FOR RV TIRE SAFETY

GREENVILLE, S.C. – RV tire maintenance experts at Michelin are offering 10 tips for RV tire safety.  Following a tire inspection routine will assure improved safety for RV owners and operators.

“Your tires are the only thing between your RV and the road, so it’s important to make sure they’re in good condition year ‘round,” said Doug Jones, customer engineering support manager for MATT.   “Making an effort to follow these simple tips now could save you and your family time, money and maybe even a life in the long run.”

- Check tires for correct air pressures.  Drivers should have an accurate pressure gauge and be instructed to check the tires on their RV each day.

- Conduct a visual inspection of your vehicle’s tires prior to operation.

- Check the vehicle’s owner’s manual or the vehicle load and tire information placard to determine precise air pressure

- Never weld or apply heat to the wheel when the tire is mounted.

- Store tires properly when they are not in use.

- Always use a safety cage when inflating tires after mounting.

- Avoid mixing tires on your vehicle – for example, pairing a normal tread depth with a deep tread depth or a bias-ply tire with a radial.

- Tire and rim servicing should be done by trained personnel using proper tools and procedures. Always have your technician dismount and inspect tires that have been running under-inflated (less than 80% of recommended pressure).

- more  -

“Most RVs have a regular maintenance program that includes checking tires, but those who do not should consider starting one immediately,” said Jones.  “Ideally, RV owners should check air pressure daily on vehicles that are in constant use.  Air pressure should be checked weekly on vehicles with less demanding schedules.”

Rapid tire wear and tire debris on highways is often caused by improperly inflated tires.  Routine maintenance maximizes tread life, minimizes downtime and improves your vehicle’s operating efficiency.

Note to editors:  An online video demonstrating preventative maintenance procedures and how to get the most value from RV tires is available at:  http://www.michelintruck.com/michelintruck/rv/rv.jsp.

Dedicated to the improvement of sustainable mobility, Michelin designs, manufactures and sells tires for every type of vehicle, including airplanes, automobiles, bicycles, earthmovers, farm equipment, heavy-duty trucks, motorcycles and the space shuttle. The company also publishes travel guides, hotel and restaurant guides, maps and road atlases. Headquartered in Greenville, S.C., Michelin North America (www.michelin-us.com) employs more than 20,900 and operates 18 major manufacturing plants in 16 locations.